## Slide 1: Serial Peripheral Interface - SPI
Dr.Sreejith Rajan

## Slide 2: SPI
SPI (Serial Peripheral Interface) is a synchronous serial communication protocol used to connect a microcontroller (Master) with one or more peripheral devices (Slaves) such as sensors, displays, and memory chips.
It was developed by Motorola and is widely used in embedded systems because it is fast, simple, and full-duplex (data can be sent and received at the same time).

## Slide 3: SPI – Common Usage
Common peripherals that use SPI:
OLED and TFT displays
Temperature and pressure sensors (BMP280, MAX6675, etc.)
Memory chips (EEPROM, Flash)
ADC and DAC Ics
SD cards

## Slide 4: SPI Protocol
1
Line | Direction | Description
MOSI | Master → Slave | Master Out, Slave In (data from master to slave)
MISO | Slave → Master | Master In, Slave Out (data from slave to master)
SCK | Master → Slave | Serial Clock (generated by master)
SS (CS) | Master → Slave | Slave Select (active LOW, selects the slave)

## Slide 5: ATMEGA 328 Pin mapping
SPI Line | AVR Pin | Arduino Pin
MOSI | PB3 | D11
MISO | PB4 | D12
SCK | PB5 | D13
SS | PB2 | D10

## Slide 6: Useful Registers
1
Register Name | Address | Purpose
SPCR | 0x2C | SPI Control Register — used to configure SPI mode and enable it
SPSR | 0x2D | SPI Status Register — shows SPI transfer status and flags
SPDR | 0x2E | SPI Data Register — holds data to transmit or receive

## Slide 7: SPCR – SPI Control Register
1
Bit | Name | Description
7 | SPIE | SPI Interrupt Enable (1 = enable interrupt on transfer complete)
6 | SPE | SPI Enable (1 = enables SPI peripheral)
5 | DORD | Data Order (0 = MSB first, 1 = LSB first)
4 | MSTR | Master/Slave Select (1 = Master mode)
3 | CPOL | Clock Polarity (0 = SCK idle low, 1 = SCK idle high)
2 | CPHA | Clock Phase (0 = sample on leading edge, 1 = sample on trailing edge)
1 | SPR1 | SPI Clock Rate Select bit 1
0 | SPR0 | SPI Clock Rate Select bit 0

## Slide 8: SPI Clock rate Table
1
SPR1 | SPR0 | SPI2X (in SPSR) | SCK Frequency
0 | 0 | 0 | fosc / 4
0 | 0 | 1 | fosc / 2
0 | 1 | 0 | fosc / 16
0 | 1 | 1 | fosc / 8
1 | 0 | 0 | fosc / 64
1 | 0 | 1 | fosc / 32
1 | 1 | 0 | fosc / 128
1 | 1 | 1 | fosc / 64

## Slide 9: SPSR – SPI Status Register
1
Bit | Name | Description
7 | SPIF | SPI Interrupt Flag (set when transfer complete)
6 | WCOL | Write Collision Flag (set if SPDR written before previous transfer ended)
5–1 | — | Reserved
0 | SPI2X | Double SPI Speed Bit (1 = double speed)

## Slide 10: Steps to configure SPI in ATMega 328 (Master) – Step1: Understand the pins
Signal | AVR Pin | Arduino Pin | Direction (Master) | Function
MOSI | PB3 | D11 | Output | Master Out Slave In
MISO | PB4 | D12 | Input | Master In Slave Out
SCK | PB5 | D13 | Output | Serial Clock
SS | PB2 | D10 | Output | Slave Select (active low)

## Slide 11: Step 2: Set the Pin directions
In master mode
MOSI, SCK, and SS must be outputs.
MISO must be input.

## Slide 12: Step3 : Enable SPI and configure as master
Bit | Field | Meaning
SPE | SPI Enable | Must be set to 1 to enable SPI
MSTR | Master Select | 1 for Master mode
SPR1, SPR0 | Clock Rate Select | Choose SPI clock speed
CPOL, CPHA | Clock Polarity & Phase | Define SPI mode (0–3)

## Slide 13: Step4 : (Optional) Double the SPI Clock Speed
If you want to increase the SPI clock, set the SPI2X bit in the SPSR register.

## Slide 14: Step 5 : Transmit and Receive Data
Use the SPDR register (SPI Data Register).
Writing to SPDR starts transmission.
Reading SPDR gives received data.
Wait for the transfer to complete by checking SPIF flag in SPSR.

## Slide 15: Step 6 : Handle the SS (Slave Select) Pin
Before sending data to a specific device:
 Pull SS low → select slave.
 Transfer data.
 Pull SS high → deselect slave

## Slide 16
THANK YOU