## Slide 1: Serial Peripheral Interface - SPI
Dr.Sreejith Rajan

## Slide 2: SPI
SPI (Serial Peripheral Interface) is a synchronous serial communication protocol used to connect a microcontroller (Master) with one or more peripheral devices (Slaves) such as sensors, displays, and memory chips.
It was developed by Motorola and is widely used in embedded systems because it is fast, simple, and full-duplex (data can be sent and received at the same time).

## Slide 3: SPI – Common Usage
Common peripherals that use SPI:
OLED and TFT displays
Temperature and pressure sensors (BMP280, MAX6675, etc.)
Memory chips (EEPROM, Flash)
ADC and DAC Ics
SD cards

## Slide 4: SPI Protocol
1
Line | Direction | Description
MOSI | Master → Slave | Master Out, Slave In (data from master to slave)
MISO | Slave → Master | Master In, Slave Out (data from slave to master)
SCK | Master → Slave | Serial Clock (generated by master)
SS (CS) | Master → Slave | Slave Select (active LOW, selects the slave)

## Slide 5: ATMEGA 328 Pin mapping
SPI Line | AVR Pin | Arduino Pin
MOSI | PB3 | D11
MISO | PB4 | D12
SCK | PB5 | D13
SS | PB2 | D10

## Slide 6: Useful Registers
1
Register Name | Address | Purpose
SPCR | 0x2C | SPI Control Register — used to configure SPI mode and enable it
SPSR | 0x2D | SPI Status Register — shows SPI transfer status and flags
SPDR | 0x2E | SPI Data Register — holds data to transmit or receive

## Slide 7: SPCR – SPI Control Register
1
Bit | Name | Description
7 | SPIE | SPI Interrupt Enable (1 = enable interrupt on transfer complete)
6 | SPE | SPI Enable (1 = enables SPI peripheral)
5 | DORD | Data Order (0 = MSB first, 1 = LSB first)
4 | MSTR | Master/Slave Select (1 = Master mode)
3 | CPOL | Clock Polarity (0 = SCK idle low, 1 = SCK idle high)
2 | CPHA | Clock Phase (0 = sample on leading edge, 1 = sample on trailing edge)
1 | SPR1 | SPI Clock Rate Select bit 1
0 | SPR0 | SPI Clock Rate Select bit 0

## Slide 8: SPI Clock rate Table
1
SPR1 | SPR0 | SPI2X (in SPSR) | SCK Frequency
0 | 0 | 0 | fosc / 4
0 | 0 | 1 | fosc / 2
0 | 1 | 0 | fosc / 16
0 | 1 | 1 | fosc / 8
1 | 0 | 0 | fosc / 64
1 | 0 | 1 | fosc / 32
1 | 1 | 0 | fosc / 128
1 | 1 | 1 | fosc / 64

## Slide 9: SPSR – SPI Status Register
1
Bit | Name | Description
7 | SPIF | SPI Interrupt Flag (set when transfer complete)
6 | WCOL | Write Collision Flag (set if SPDR written before previous transfer ended)
5–1 | — | Reserved
0 | SPI2X | Double SPI Speed Bit (1 = double speed)

## Slide 10: Steps to configure SPI in ATMega 328 (Master) – Step1: Understand the pins
Signal | AVR Pin | Arduino Pin | Direction (Master) | Function
MOSI | PB3 | D11 | Output | Master Out Slave In
MISO | PB4 | D12 | Input | Master In Slave Out
SCK | PB5 | D13 | Output | Serial Clock
SS | PB2 | D10 | Output | Slave Select (active low)

## Slide 11: Step 2: Set the Pin directions
In master mode
MOSI, SCK, and SS must be outputs.
MISO must be input.

## Slide 12: Step3 : Enable SPI and configure as master
Bit | Field | Meaning
SPE | SPI Enable | Must be set to 1 to enable SPI
MSTR | Master Select | 1 for Master mode
SPR1, SPR0 | Clock Rate Select | Choose SPI clock speed
CPOL, CPHA | Clock Polarity & Phase | Define SPI mode (0–3)

## Slide 13: Step4 : (Optional) Double the SPI Clock Speed
If you want to increase the SPI clock, set the SPI2X bit in the SPSR register.

## Slide 14: Step 5 : Transmit and Receive Data
Use the SPDR register (SPI Data Register).
Writing to SPDR starts transmission.
Reading SPDR gives received data.
Wait for the transfer to complete by checking SPIF flag in SPSR.

## Slide 15: Step 6 : Handle the SS (Slave Select) Pin
Before sending data to a specific device:
 Pull SS low → select slave.
 Transfer data.
 Pull SS high → deselect slave

## Slide 16: Data Transfer in SPI

## Slide 17: How SPIF is cleared ?
SPIF becomes 1 when the data transfer is complete
SPIF is automatically cleared when we read SPDR( or copy the SPDR Value to a variable)
That means we do not need to clear SPIF manually. It will be done when we read the SPDR value(That means we must read SPDR)

## Slide 18: BMP 280
The BMP280 is a digital barometric pressure and temperature sensor made by Bosch Sensortec. It’s widely used in embedded systems and IoT applications like:
  Altimeters
  Weather monitoring
  Environmental sensing
  Smart watches and wearables
  It can communicate via I²C or SPI, making it easy to interface with microcontrollers like the ATmega328

## Slide 19: Electrical Parameters
Parameter | Typical Value | Notes
Operating Voltage | 1.71V – 3.6V | Often powered from 3.3V
Interface | I²C or SPI | Selectable by CSB pin
Pressure Range | 300 hPa – 1100 hPa | Equivalent to 9,000 m to -500 m altitude
Temperature Range | -40°C to +85°C | Suitable for most embedded systems
Resolution | 0.16 Pa (pressure), 0.01°C (temp) | Very precise
Supply Current | ~2.7 µA (normal mode) | Very low power

## Slide 20: BMP 280 Pinout
Pin | Full Name | Description | Connect To (ATmega328)
SCL | Serial Clock | SPI clock line | PB5 (SCK)
SDA | Serial Data | MOSI (Master-Out Slave-In) | PB3 (MOSI)
SDO | Serial Data Out | MISO (Master-In Slave-Out) | PB4 (MISO)
CSB | Chip Select Bar | Active-low select pin | PB2 (SS) or any digital output you control as CS
VCC | Power | 3.3 V supply | 3.3 V
GND | Ground | Common ground | GND

## Slide 21: Reading and Writing –BMP 280
Operation | Meaning
Write | The microcontroller sends data to the BMP280 to set something — like a configuration, control command, or reset.
Read | The microcontroller asks the BMP280 to send back data — like sensor readings or status information.
 These operations are done through registers inside the BMP280.
Each register in the BMP280 is like a small “memory box” with an address and a stored value.

## Slide 22: Reading and Writing –BMP 280
Bit | 7 | 6–0
Meaning | R/W bit | Register address (7 bits)
Bit 7  0 Means Write operation
Bit 7 1 Means Read operation

## Slide 23: Role of Registers in BMP 280
Register | Address | Purpose
Chip ID | 0xD0 | Read-only, fixed value 0x58
Reset | 0xE0 | Write-only, write 0xB6 to reset
Status | 0xF3 | Shows if measurement is running
Ctrl_Meas | 0xF4 | Controls oversampling and power mode
Config | 0xF5 | Filter and standby settings
Data registers | 0xF7–0xFC | Raw pressure and temperature data

## Slide 24: Read the Chip id of BMP 280

## Slide 25
THANK YOU