## Slide 1: LM 35 Temperature Sensor -ADC
Dr.Sreejith Rajan

## Slide 2: ADC
  Digital Value = (Vis / Aref) x 1024
  Eg : if Vis= 2v and Aref= 5v
  Digital Value = (2/5) x1024
  = 409
  Input signal voltage = Vis = (Digital Value X Aref )/1024;
1

## Slide 3: LM 35 Temperature sensor with Arduino

## Slide 4: LM 35 Temperature sensor with Arduino

## Slide 5: Read Temperature and Display
Use basic math to convert ADC Value to Temperature
Use lcd.h and lcd.c to print temperature in the LCD
  Input signal voltage = Vis = (Digital Value X Aref )/1024;
  Temperature = Vis/ 10mv
  = Digital Value X [(Aref X 100)/1024]
  = Digital Value X [(5 X 100)/1024]
  = Digital Value X 0.488

## Slide 6
THANK YOU